## Slide 1: Videos 1, 2, & 3: Review
By the end of Videos 1, 2, and 3, we want to be able to answer:
  What long-term pavement condition should we plan for?
  Which type of pavement “treatments” or “repairs” are acceptable?
    Should we use surface treatments?
  Which program services should be prioritized?
  Should arterials/collectors be prioritized differently than local access streets?

## Slide 2: Video #3: Pavement Goals & Methods of Repair
Streets Sustainability Committee

## Slide 3: Video #3 Overview
Discuss
Discuss the different pavement condition ranges
Review
Review different “treatment” or “repair” methods (historical & future)
Lower cost treatments with shorter life-cycles versus
Higher cost treatments with longer life-cycles
Review
Review how pavement condition & treatment types affect cost

## Slide 4: As we review examples, a few considerations:
Not all conditions age at the same rate
PMP principle: its cheaper to maintain than to rebuild
Slower aging & deterioration
Slower aging & deterioration
Faster aging & deterioration
Today

## Slide 5: Pavement condition examples: What’s an acceptable pavement condition?
McDonald Road (South of Sprague Ave.)
PCI Range 85-100
Minimal surface defects: negligible crack fill/longitudinal cracks/utility patches.
Road Age: 6 years old (2015 Reconstruction Project)

## Slide 6: Pavement condition examples: What’s an acceptable pavement condition?
University Road (Between 8th & 16th Ave.)
PCI Range 75-80
Noticeable surface cracking (crack fill), negligible bumps/depressions
Road Age: 9 years old (2012 Overlay Project)

## Slide 7: Pavement condition examples: What’s an acceptable pavement condition?
Alki Ave (Between Best Rd and Adams Rd.)
PCI Range 75-80
Surface weathering, edge cracking at shoulder, occasional longitudinal cracking/bumps
Road Age: 15 years old (2006 Sewering Project)

## Slide 8: Pavement condition examples: What’s an acceptable pavement condition?
Grace Ave. (Between University Rd. and Bowdish Rd.)
PCI Range 65-70
Longitudinal cracking and occasional transverse cracking, early settling at manhole will lead to local failures (blow-outs leading to potholes), edge cracking at shoulder, utility patching
Road Age: 24 years old (1997 Sewering Project)

## Slide 9: Pavement condition examples: What’s an acceptable pavement condition?
3rd Avenue (Between Havana Rd. & Carnahan Rd.)
PCI Range 60-65
Extensive surface cracking (see longitudinal wheel path cracks), measurable local failures like rutting or potholes and patches, susceptible to freeze/thaw damage
Road Age: 19 years old (2002 Sewering Project)

## Slide 10: Pavement condition examples: What’s an acceptable pavement condition?
Intersection of Ponderosa & Bates
PCI Range 55-60
Areas of asphalt failure (alligatored cracking), measurable local failures like sunken/failed manhole patches (bumps), multiple utility patches, susceptible to freeze/thaw damage
Road Age: 21 years old (2000 Sewering Project)

## Slide 11: Pavement condition examples: What’s an acceptable pavement condition?
Calvin Rd. (North of Wellesley Ave.)
PCI Range 45-50
Extensive surface (alligatored) cracking, measurable local failures: failed utility trench patches (bumps), longitudinal and transverse cracks, susceptible to freeze/thaw damage
Road Age: 36 years old (1985 Residential Development)

## Slide 12: Pavement condition examples: What’s an acceptable pavement condition?
Vera Crest Dr. (North of 24th Ave.)
PCI Range 20-25
Complete pavement failure: full width alligatored cracking, extensive patching, extensive pothole repair (bumps), susceptible to freeze/thaw damage
Road Age: 30 years old (1991 Residential Development)

## Slide 13: Which pavement “treatments” or “repairs” are considered?

## Slide 14: Which pavement “treatments” or “repairs” are considered?
Methods for maintaining our streets
  Preventative maintenance
    Spot repair, patching, crack seal
  Surface Treatments
    Most effective on locals/collectors
  Rehabilitation
    Grind/Overlay street surface
  Reconstruction
    Remove/Replace street
Current practice

## Slide 15: How can surface treatments help?

## Slide 16
Typically work well on “good” condition roads
Slows aging = longer life = save money
Easy to implement
New wearing surface for traffic
Protects the street against:
  Weathering
  Surface cracking
  Prevents potholes
Concerns:
  Longevity
  Availability
  Public acceptance
$5-10/SY
Surface Treatments
$30-80/SY
Rehabs & Rebuilds
Surface Treatments

## Slide 17: Which surface treatments have been used in our region?
  Fog Seals
  Chip Seals
  Slurry Seals & Microsurfacing
  Thin overlays

## Slide 18: How can surface treatments help?
Sunscreens and moisturizers
  Fog seals
  Rejuvenators
Padded layers = extra protection
  Chip seals
  Slurry seals
  Microsurfacing
Full body armor
  Double chip seals
  Combo seals (from above)
  Thin overlays
Intensity & Cost
$
$$$$
All streets with PCI 40-80 that may be considered for surface treatments.

## Slide 19: How do pavement condition and available “treatment” methods impact long-term costs for the PMP?
Less $
More $$$
Preservation: $10 Mil/Yr
Maintenance: $6 Mil/Yr
Total: $16 Mil/Yr

## Slide 20: Available resources determine available options
What is the condition of the pavement?
What is the best “treatment” to extend the pavement life most effectively?
What is our condition goal and available budget?
Which streets should be prioritized to maximize benefit?
Prioritized project list generated

## Slide 21: How far can our dollars take us?

## Slide 22: How far can our dollars take us?
Chart: Local Access Streets
| 0 | 1 | 2 | 3 | 4 | 5
Budget to Maintain PCI ($6.5 M/Yr) | 76 | 76.21 | 76.28 | 76 | 76.18 | 76.15
Today's Budget ($2 M/Yr) | 76 | 73.28 | 70.77 | 68.07 | 65.26 | 62.1
Today’s Budget
($1.5-2.0 M/Yr)
Budget for Constant PCI ($6.5 M/Yr)
Regardless of reduced budget amount, it takes at least $6.5 M/Yr to stop the decline.
Notes: -Each PCI point costs about $300,000: $6.5-2 = 4.5M, 76-62=14. 4,500,000/14=$321,428 per PCI point
-There is nuance with dollar projections and PCI impacts because we spend 101 funds on specific patches

## Slide 23: How far can our dollars take us?
Chart: Arterial & Collector Streets
| 0 | 1 | 2 | 3 | 4 | 5
Budget to Maintain PCI ($3.5 M/Yr) | 77 | 77 | 77.49 | 77 | 77 | 77
Today’s Budget =
Budget for Constant PCI
($3.5-4.0 M/Yr)
On average, the City has expended funds to maintain its arterial and collector streets in their current condition.

## Slide 24: How to fund the PMP to reflect our priorities?

## Slide 25: How to fund the PMP to reflect our priorities?
Less $
More $
Asphalt Preservation
Cost to keep existing condition: $10 M/Yr
  Locals $6.5 M/Yr
  Arterials/Collectors: $3.5 M/Yr
  $5 M/Yr dedicated funds
    $3 M/Yr local funds + $2 M/Yr grant funds
  $5 M/Yr annual shortfall covered by reducing services
Street Maintenance
Cost to maintain existing services: $6 M/Yr
  $3 M/Yr dedicated funds
  $3 M/Yr annual shortfall covered by reserves
Preservation: $10 Mil/Yr
Maintenance: $6 Mil/Yr
Total: $16 Mil/Yr

## Slide 26: Key Considerations
Videos 1, 2, and 3 have provided the background info to consider the following:
  What long-term pavement condition should we plan for?
  Which type of pavement “treatments” or “repairs” are acceptable?
    Should we use surface treatments?
  Which program services should be prioritized?
  Should arterials/collectors be prioritized differently than local access streets?

## Slide 27
Streets Sustainability Committee
For more information:
https://www.spokanevalley.org/StreetsCommittee
Adam Jackson, Pavement Management Program Coordinator
509-720-5024
Ajackson@SpokaneValley.org
StreetSolutions@SpokaneValley.org